## Slide 1: NetLock: Fast, Centralized Lock Management Using Programmable Switches
Zhuolong Yu
Yiwen Zhang, Vladimir Braverman, Mosharaf Chowdhury, Xin Jin

## Slide 2: Increasing demand of database services
Lock managers are a critical building block of cloud databases

## Slide 3: The lifetime a transaction
Lock Manager
Can I read/write that resource?
Let me check…

## Slide 4: The lifetime a transaction
Lock Manager
Read
Write

## Slide 5: The lifetime a transaction
Lock Manager
Read
Write
Ok, I’ll release it
I’m done with the resource

## Slide 6: The lifetime a transaction
In-memory database, RDMA networks
(FaRM [SOSP’15], DrTM [SOSP’15])
Lock Manager
Read
Write
I can read/write very fast now. Can the LM be faster?
I will …….. try

## Slide 7: Performance and policy support
Can we have both?
 | High performance | Policy support
Centralized lock manager | Bottleneck at the server’s capacity | Flexible
Decentralized lock manager | Usually good | Hard to support
DSLR [sigmod’18] avoids starvation in a decentralized manner, but it cannot support other policies.
DrTM [sosp’15] uses blind fail-and-retry
high client CPU usage
Exponential back-off
high latency
Distributed queues
extra network round-trips

## Slide 8: PISA: Protocol Independent Switch Architecture
Programmable switch
Then we can have both advantages!
What if we implement the centralized lock manager in a switch?
Eliminate the bottleneck at the lock server

## Slide 9: PISA: Protocol Independent Switch Architecture
Match + Action
Programmable Parser
Programmable Match-Action Pipeline
Memory
ALU
…
…
…
…
Programmable Parser
  Parse custom key-value fields in the packet
Programmable Match-Action Pipeline
  Read and update key-value data at line rate

## Slide 10: Design goals for NetLock
High throughput
Low latency
Flexible policy support
Challenges:
Limited memory to store the locks
Limited functionalities to process the locks and realize the policies
They are directly achieved by using high performance switches, and a centralized approach.

## Slide 11: NetLock architecture
NetLock processes lock requests with a combination of switch and servers.
The switch only stores and processes the requests on popular locks.
NetLock is incrementally deployable and compatible with existing datacenter networks.

## Slide 12: Packet format
ETH | IP | UDP | Action type | Lock ID | Lock mode | Txn. ID
L2/L3 routing
reserved port #
Existing Protocols
NeLock Applications
Acquire / Release
Shared / Exclusive

## Slide 13: Memory layout
ETH | IP | UDP | Action type | Lock ID | Lock mode | Txn. ID
Circular queues
Extra register to keep the head and tail pointers

## Slide 14: Memory layout
All the locks share a large queue
Extra registers to store the boundaries

## Slide 15: Memory allocation
Process as many lock requests in the switch as possible
Clients send lock requests to NetLock without knowing where the requests will be processed
NetLock memory allocation

## Slide 16: Processing the locks
S
S
S
E
S
I want to read
Write
R
I am done
R
R
R
W
E
S
S
S
Only one memory access (read/write) to a register array upon one packet
Release
Resubmit and notify

## Slide 17: Policy support
Starvation-freedom
  The requests are in a FCFS queue
Service differentiation with priority
  One priority per stage
  Low-priority can be offloaded to the lock servers
Performance Isolation
  A rate limiter is implemented to enforce a quota for each tenant

## Slide 18: Evaluation
Testbed
  6.5 Tbps Barefoot Tofino switch
  12 servers with an 8-core CPU and a 40G NIC
Comparison
  DSLR, DrTM (RDMA based)
  NetChain (Programmable Switch)
Workload
  Microbenchmark (simple lock requests)
  TPC-C with 1/10 warehouse per node

## Slide 19: Evaluation
How fast can NetLock process lock requests?
What’s the benefit of NetLock on transaction performance over existing solutions?
Can NetLock provide flexible policy support?
How’s does NetLock handle failures?
This talk

## Slide 20: Evaluation: Microbenchmark
12 servers cannot saturate the switch which is able to process billions of packets per second.

## Slide 21: Evaluation: Transaction performance
NetLock improves the throughput by 14.0-18.4x compared with DSLR.

## Slide 22: Evaluation: Transaction performance
NetLock also reduces the latency by 4.7-20.3x compared with DSLR.

## Slide 23: Evaluation: Service differentiation
Two clients get similar throughput regardless of priority
High priority client gets much higher throughput

## Slide 24: Evaluation: Performance isolation
Tenant 1 has 7 clients
Tenant 2 has 3 clients
After enforcing isolation, two tenants get similar throughput.

## Slide 25: Conclusion
NetLock is a centralized lock manager
Co-design programmable switches and servers
Provide high performance and flexible policy support

## Slide 26: Thank you